PO3_DGW_Digital watch

        (GDD)

Table 1 Status Table
Document Name	Author	Version	Update Date	Status
GDD	Norhan Nassar	1.3	12/03/2020	Proposed

DOCUMENT HISTORY
Table 2 Document History
Version	Description of Change	Author	Date	Document Status
1	Initial creation of GDD Document	Norhan Nassar	27/01/2020	Draft
1.1	Adding Software input output, / Updating Software feature diagram and updating static layered architecture	Norhan Nassar	1/03/2020	Proposed
1.2	Adding Requirement at LCD Component / Req_PO3_DGW_GDD_11_V01.0 and shifting other Requirements ids	Norhan Nassar	4/03/2020	Proposed
1.3	Updating Feature Diagram, Return type of all Requirements, Deleting some Requirements at LCD Component	Norhan Nassar	12/3/2020	Proposed

Table 3 Reference Table
Reference Input Documents	Version	Status
SRS	1.7	Proposed

# Project Description
Digital Watch System that has three different modes.
1. Time Display Mode that displays the time as a normal clock and increments its time every 1 second.
2. Alarm Mode that it turns a buzzer on when time is on.
3. Stopwatch Mode.
The user can select an option of these three modes.
# Software Context Diagram

# Input Output Signals
3.1 Input Output Diagram

3.2 Input output Table
Inputs	Name	Range		Unit
	Sig_Button1_Mode	0:2	NA
	Sig_Button2	0:1	NA
	Sig_Button3	0:1	NA
	Sig_HrVar	0:12	Time-Hours
	Sig_MinVar	0:60	Time-Minutes
	Sig_SecVar	0:60	Time_Seconds
	Sig_CL	0:1	Am/Pm
	Sig_SetCell	0:16	NA
	Sig_AlHrVar	0:12	Time-Hours
	Sig_AlMinVar	0:60	Time-Minutes
	Sig_AlSecVar	0:60	Time-Seconds
	Sig_AlCL	0:1	Am/Pm
	Sig_AlSetCell	0:16	NA
	Sig_SwHrVar	0:12	Time-Hours
	Sig_SwMinVar	0:60	Time-Minutes
	Sig_SwSecVar	0:60	Time-Seconds
	Sig_Status	0:1	NA
	Sig_Reset	0:1	NA
	Sig_SecVar	0:60	Time-Seconds
Outputs	Name	Range	Unit
	Sig_Buzzer	0:1	NA

# Software Feature:

# Static Architecture:

# 6 Requirements
## 6.1 MCAL Layer:
## 6.1.1 DIO Component:

Req_ID	Req_PO3_DGW_GDD_01_V01.0		Covers		____________
Author	Norhan Nassar		Date	1/03/2020
Description:	Set Pin Direction for certain Port
API	STD_ERORR DIO_SetPinDirection(u8 Copy_u8Port,u8 Copy_u8Pin, u8 Copy_u8Direction)
Parameters	Type	Name			Description
	u8 / u8 / u8	Copy_u8Port / Copy_u8Pin / Copy_u8Direction			Port from ‘A’ to ‘D’ as Ascii code / Pin from 0 to 7 / Output -> 1 or input -> 0
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_02_V01.0		Covers		__________
Author	Norhan Nassar		Date	1/03/2020
Description:	Set or Reset Pin at certain port
API	STD_ERORR DIO_SetPinValue(u8 Copy_u8Port,u8 Copy_u8Pin, u8 Copy_u8Value);
Parameters	Type	Name			Description
	u8 / u8 / u8	Copy_u8Port / Copy_u8Pin / Copy_u8Value			Port from ‘A’ to ‘D’ as Ascii code / Pin from 0 to 7 / Value -> 1 to set Pin high / Value -> 0 to set Pin low
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_03_V01.0		Covers		____________
Author	Norhan Nassar		Date	1/03/2020
Description:	Get Pin value at certain Port / 1 -> High / 0 -> Low
API	STD_ERORR DIO_GetPinVal(u8 Copy_u8Port,u8 Copy_u8Pin,u8* Copy_PtrVal)
Parameters	Type	Name			Description
	u8 / u8 / u8*	Copy_u8Port / Copy_u8Pin / Copy_PtrVal			Port from ‘A’ to ‘D’ as Ascii code / Pin from 0 to 7 / Pointer to return the status of the pin in it
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

### 6.1.2 Port Component:

Req_ID	Req_PO3_DGW_GDD_04_V01.0		Covers		___________
Author	Norhan Nassar		Date	1/03/2020
Description:	It initialize each Port and Pins to be output or input according to Port_config file / Output -> 1 Input -> 0
API	STD_ERORR Port_Initialize(void);
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

### 6.1.3 Timer Component:

Req_ID	Req_PO3_DGW_GDD_05_V01.0		Covers		Req_PO3_DGW_SRS_01_V01.2 / Req_PO3_DGW_SRS_02_V01.2 / Req_PO3_DGW_SRS_20_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It makes Timer start to increment.
API	STD_ERORR Timer_Init(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_06_V01.0		Covers		Req_PO3_DGW_SRS_01_V01.2 / Req_PO3_DGW_SRS_02_V01.2 / Req_PO3_DGW_SRS_20_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It will display HrVar, MinVar, Secvar and CycleLength / And it will take which cell to display onto the LCD the it called LCD / to write these data onto this location.
API	STD_ERORR Timer_SetCallBack(void(*Copy_pvCallBackPtr)(void))
Parameters	Type	Name			Description
	void (*) (void)	Copy_pvCallBackPtr			Pointer to function that it will be implemented when Interrupt has been happened.
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

## 6.2 HAL Layer:
# 6.2.1 Switch Component:
Req_ID	Req_PO3_DGW_GDD_07_V01.0		Covers		Req_PO3_DGW_SRS_09_V01.2 / Req_PO3_DGW_SRS_10_V01.2 / Req_PO3_DGW_SRS_14_V01.2 / Req_PO3_DGW_SRS_21_V01.2 / Req_PO3_DGW_SRS_23_V01.2 / Req_PO3_DGW_SRS_24_V01.2 / Req_PO3_DGW_SRS_25_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	Get Switch state according to its config file that it configures its Port and pin to get its status
API	STD_ERORR Switch_GetState (u8 Copy_u8SwNum,u8* Copy_ptrState)
Parameters	Type	Name			Description
	u8 / u8*	Copy_u8SwNum / Copy_ptrState			Switch Number to get state of a certain switch / Pointer to state of the switch according to Switch_config file / Pressed will represent 0 or 1 / If RELEASE_STATE defined as 1 / So pressed will represent 0 / If RELEASE_STATE defined as 0 / So pressed will represent 1
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

# 6.2.2 Buzzer Component:

Req_ID	Req_PO3_DGW_GDD_08_V01.0		Covers		Req_PO3_DGW_SRS_03_V01.2 / Req_PO3_DGW_SRS_04_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It sets buzzer state according to its config file that it congiures its port and pin.
API	STD_ERORR Buzzer_SetState(u8 State)
Parameters	Type	Name			Description
	u8	State			Buzzer state to set its pin to this state / High -> 1 / Low -> 0
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

6.2.3 LCD Component:

Req_ID	Req_PO3_DGW_GDD_09_V01.0		Covers		Req_PO3_DGW_SRS_06_V01.2 / Req_PO3_DGW_SRS_08_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It clears the screen.
API	STD_ERORR CLCD_Clear(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_10_V01.0		Covers		Req_PO3_DGW_SRS_06_V01.2 / Req_PO3_DGW_SRS_08_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It takes Pointer to char of the string that it will be written as whole onto the LCD.
API	STD_ERORR CLCD_WriteString(const char* Copy_pchString);
Parameters	Type	Name			Description
	const char*	Copy_pchString			Pointer to char of the string to be written onto LCD
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_11_V01.0		Covers		Req_PO3_DGW_SRS_10_V01 / Req_PO3_DGW_SRS_11_V01.2 / Req_PO3_DGW_SRS_12_V01.2 / Req_PO3_DGW_SRS_13_V01.2 / Req_PO3_DGW_SRS_15_V01.2 / Req_PO3_DGW_SRS_16_V01.2 / Req_PO3_DGW_SRS_17_V01.2 / Req_PO3_DGW_SRS_18_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It sets new position for the LCD to start write from. / XPos -> which column / YPos -> which Row / To select which cell.
API	STD_ERORR CLCD_GoToXYPos(u8 Copy_u8XPos,u8 Copy_u8YPos);
Parameters	Type	Name			Description
	u8 / u8	Copy_u8XPos / Copy_u8YPos			XPos -> which column / YPos -> which row
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_12_V01.0		Covers		Req_PO3_DGW_SRS_06_V01.2 / Req_PO3_DGW_SRS_08_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It writes number onto the LCD.
API	STD_ERORR CLCD_WriteNum (u32 Copy_u32Num);
Parameters	Type	Name			Description
	u32	Copy_u32Num			Number to be written onto the LCD
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

## 6.3 APP Layer
## 6.3.1 Time-Display Component

Req_ID	Req_PO3_DGW_GDD_13_V01.0		Covers		Req_PO3_DGW_SRS_02_V01.2 / Req_PO3_DGW_SRS_10_V01.2 / Req_PO3_DGW_SRS_14_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It displays HrVar, MinVar, Secvar and CycleLength / And it takes which cell to display onto the LCD.
API	STD_ERORR Time_Display(u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Certain Position to start write from onto the LCD
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_14_V01.0		Covers		Req_PO3_DGW_SRS_11_V01.2 / Req_PO3_DGW_SRS_12_V01.2 / Req_PO3_DGW_SRS_13_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It adjusts the cursor position at LCD.
API	STD_ERORR Time_AdjustCursor (u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Pointer to Certain Position
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_15_V01.0		Covers		Req_PO3_DGW_SRS_14_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It increments Hrvar, SecVar and MinVar according to which cell LCD on at this time.
API	STD_ERORR Time_Incr(u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Pointer to Certain Position
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

### 6.3.2 Alarm mode requirements

Req_ID	Req_PO3_DGW_GDD_16_V01.0		Covers		Req_PO3_DGW_SRS_15_V01.2 / Req_PO3_DGW_SRS_16_V01.2 / Req_PO3_DGW_SRS_17_V01.2 / Req_PO3_DGW_SRS_18_V01.2 / Req_PO3_DGW_SRS_19_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It displays AlHrVar, AlMinVar, AlSecvar and AlCycleLength / And it takes which cell to display onto the LCD.
API	STD_ERORR Alarm_Display(u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Certain Position to start write from onto the LCD
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_17_V01.0		Covers		Req_PO3_DGW_SRS_15_V01.2 / Req_PO3_DGW_SRS_16_V01.2 / Req_PO3_DGW_SRS_17_V01.2 / Req_PO3_DGW_SRS_18_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It adjusts the cursor position at LCD.
API	STD_ERORR Alarm_AdjustCursor (u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Pointer to Certain Position
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_18_V01.0		Covers		Req_PO3_DGW_SRS_19_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It increments AlHrvar, AlSecVar and AlMinVar according to which cell LCD on at this time.
API	STD_ERORR Alarm_Incr(u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Pointer to Certain Position
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

### 6.3.3 Stop-Watch Component

Req_ID	Req_PO3_DGW_GDD_19_V01.0		Covers		Req_PO3_DGW_SRS_22_V01.2 / Req_PO3_DGW_SRS_23_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It displays StHrVar, StMinVar, StSecvar. / And it takes which cell to display onto the LCD.
API	STD_ERORR SW_Display(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_20_V01.0		Covers		Req_PO3_DGW_SRS_21_V01.2 / Req_PO3_DGW_SRS_22_V01.2 / Req_PO3_DGW_SRS_23_V01.2 / Req_PO3_DGW_SRS_24_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It checks which press at this time / First press -> start SW -> Set SW_flag = 1 to start increment / Second press -> Stop SW -> Stopwatch_flag = 1 to reset / Thirs press -> Resume SW_flag = 0
API	STD_ERORR SW_CheckStatus(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_20_V01.0		Covers		Req_PO3_DGW_SRS_25_V01.2 / Req_PO3_DGW_SRS_26_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It Resets SW_flag and StopWatch_flag
API	STD_ERORR SW_Reset(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

### 6.3.4 DGW Requirements

Req_ID	Req_PO3_DGW_GDD_21_V01.0		Covers		Req_PO3_DGW_SRS_06_V01.2 / Req_PO3_DGW_SRS_09_V01.2 / Req_PO3_DGW_SRS_10_V01.2 / Req_PO3_DGW_SRS_21_V01.2 / Req_PO3_DGW_SRS_23_V01.2 / Req_PO3_DGW_SRS_25_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It reads Button 1 switch state and modifies Current_Mode signal to detect which mode is running know (Time or Alarm or Stop Watch) / Current_Mode is a global variable.
API	STD_ERORR ReadMode(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_22_V01.0		Covers		Req_PO3_DGW_SRS_02_V01.2 / Req_PO3_DGW_SRS_06_V01.2 / Req_PO3_DGW_SRS_07_V01.2 / Req_PO3_DGW_SRS_10_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It checks Current_Mode signal to choice which to display -> Time or Alarm or Stopwatch. / Current_Mode is a global variable.
API	STD_ERORR Display(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_23_V01.0		Covers		Req_PO3_DGW_SRS_11_V01.2 / Req_PO3_DGW_SRS_12_V01.2 / Req_PO3_DGW_SRS_13_V01.2 / Req_PO3_DGW_SRS_15_V01.2 / Req_PO3_DGW_SRS_16_V01.2 / Req_PO3_DGW_SRS_17_V01.2 / Req_PO3_DGW_SRS_18_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It reads Button 2 switch state / If (Pressed) -> Check Current_Mode signal to detect which mode is running know. / If (Current_Mode == 0) -> call Time_voidAdjustCursor() / If (Current_Mode == 1) -> call Alarm_voidAdjustCursor() / If (Current_Mode == 2) -> call SW_voidCheckstatus() / Current_Mode is a global variable.
API	STD_ERORR ReadPos(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_24_V01.0		Covers		Req_PO3_DGW_SRS_14_V01.2 / Req_PO3_DGW_SRS_19_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It reads Button 3 switch state / If (Pressed) -> Check Current_Mode signal to detect which mode is running know. / If (Current_Mode == 0) -> call Time_voidIncr() / If (Current_Mode == 1) -> call Time_voidIncr() / If (Current_Mode == 2) -> call SW_voidReset() / Current_Mode is a global variable.
API	STD_ERORR ReadInc(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_25_V01.0		Covers		Req_PO3_DGW_SRS_20_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It checks Buzzer_signal / If (Buzzer_signal ) -> turn Buzzer on / If (Buzzer_signal) -> turn Buzzer off / Buzzer_signal is a global variable.
API	STD_ERORR CheckBuzzerState(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly

Req_ID	Req_PO3_DGW_GDD_26_V01.0		Covers		Req_PO3_DGW_SRS_01_V01.2 / Req_PO3_DGW_SRS_02_V01.2 / Req_PO3_DGW_SRS_03_V01.2
Author	Norhan Nassar		Date	27/2/2020
Description:	It increments HrVar, MinVar and SecVar every 1 sec by passing this function to the ISR of the timer. / And it checks Current_Mode signal / If(Current_Mode == 1) -> Alarm Mode / So if (HrVar,MinVar and SecVar == AlHrVar, AlMinVar and AlSecVar ) / Buzzer_signal = 1
API	STD_ERORR TimeInc(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	STD_ERORR	_____			STD_ERORR / OK -> if the function works correctly / NOT_OK -> if the function doesn’t work correctly