PO3_DGW_Digital watch

        (GDD)

Table 1 Status Table
Document Name	Author	Version	Update Date	Status
GDD	Norhan Nassar	1.0	27/02/2020	Draft

DOCUMENT HISTORY
Table 2 Document History
Version	Description of Change	Author	Date	Document Status
1	Initial creation of GDD Document	Norhan Nassar	27/01/2020	Draft

# Project Description
Digital Watch System that has three different modes.
1. Time Display Mode that displays the time as a normal clock and increments its time every 1 second.
2. Alarm Mode that it turns a buzzer on when time is on.
3. Stopwatch Mode.
The user can select an option of these three modes.
# Software Context Diagram

# Software Feature:

# Static Architecture:

# Requirements
## MCAL Layer:
### DIO Component:

Req_ID	Req_PO3_DGW_GDD_01_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	Set Pin Direction for certain Port / Output -> 1 Input -> 0
API	SetPinDirection(u8 Copy_u8Port,u8 Copy_u8Pin, u8 Copy_u8Direction)
Parameters	Type	Name			Description
	u8 / u8 / u8	Copy_u8Port / Copy_u8Pin / Copy_u8Direction			Port from A to D / Pin from 0 to 7 / Output -> 1 or input -> 0
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_02_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	Set or Reset Pin at certain port / Value -> 1 to set it high / Value -> 0 to reset it to low
API	SetPinValue(u8 Copy_u8Port,u8 Copy_u8Pin, u8 Copy_u8Value);
Parameters	Type	Name			Description
	u8 / u8 / u8	Copy_u8Port / Copy_u8Pin / Copy_u8Value			Port from A to D / Pin from 0 to 7 / Value -> 1 to set Pin high / Value -> 0 to set Pin low
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_03_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	Get Pin value at certain Port / 1 -> High / 0 -> Low
API	GetPinVal(u8 Copy_u8Port,u8 Copy_u8Pin)
Parameters	Type	Name			Description
	u8 / u8	Copy_u8Port / Copy_u8Pin			Port from A to D / Pin from 0 to 7
Return	Type	Name			Description
	u8	_____			Return <- Status of the Pin

### Port Component:

Req_ID	Req_PO3_DGW_GDD_04_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	IT initialize each Port and Pins to be output or input according to Port_config file / Output -> 1 Input -> 0
API	PortInitialize(void);
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

### Timer Component:

Req_ID	Req_PO3_DGW_GDD_05_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It makes Timer start to increment.
API	Timer_voidInit(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_06_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It will display HrVar, MinVar, Secvar and CycleLength / And it will take which cell to display onto the LCD the it called LCD / to write these data onto this location.
API	Timer_voidSetCallBack(void(*Copy_pvCallBackPtr)(void))
Parameters	Type	Name			Description
	void (*) (void)	Copy_pvCallBackPtr			Pointer to function that it will be implemented when Interrupt has been happened.
Return	Type	Name			Description
	void	_____			_____

## HAL Layer:
# 5.2.1 Switch Component:

Req_ID	Req_PO3_DGW_GDD_07_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	Get Switch state according to its config file that it configures its Port and pin to get its status
API	Switch_u8GetState (u8 Copy_u8SwNum)
Parameters	Type	Name			Description
	u8	Copy_u8SwNum			Switch Number to get state of a certain switch
Return	Type	Name			Description
	u8	_____			Return = State of the switch according to Switch_config file / Pressed will represent 0 or 1 / If RELEASE_STATE defined as 1 / So pressed will represent 0 / If RELEASE_STATE defined as 0 / So pressed will represent 1

# 5.2.2 Buzzer Component:

Req_ID	Req_PO3_DGW_GDD_09_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It sets buzzer state according to its config file that it congiures its port and pin.
API	Buzzer_voidSetState(u8 State)
Parameters	Type	Name			Description
	u8	State			Buzzer state to set its pin to this state / High -> 1 / Low -> 0
Return	Type	Name			Description
	void	_____			_____

5.2.3 LCD Component:

Req_ID	Req_PO3_DGW_GDD_10_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	Initialize LCD according to its datasheet.
SWC Interface	CLCD_voidInitialize(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_11_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	Set data on data port of the LCD.
SWC Interface	CLCD_voidWriteData(u8 Copy_u8Data)
Parameters	Type	Name			Description
	u8	Copy_u8Data			Data
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_12_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It takes Pointer to char of the string that it will be written as whole onto the LCD.
SWC Interface	CLCD_voidWriteString(const char* Copy_pchString);
Parameters	Type	Name			Description
	const char*	Copy_pchString			Pointer to char of the string to be written onto LCD
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_13_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It sets new position for the LCD to start write from. / XPos -> which column / YPos -> which Row / To select which cell.
SWC Interface	CLCD_voidGoToXYPos(u8 Copy_u8XPos,u8 Copy_u8YPos);
Parameters	Type	Name			Description
	u8 / u8	Copy_u8XPos / Copy_u8YPos			XPos -> which column / YPos -> which row
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_14_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It writes number onto the LCD.
SWC Interface	CLCD_voidWriteNum (u32 Copy_u32Num);
Parameters	Type	Name			Description
	u32	Copy_u32Num			Number to be written onto the LCD
Return	Type	Name			Description
	void	_____			_____

## APP Layer
## 5.3.1 Time-Display Component

Req_ID	Req_PO3_DGW_GDD_15_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It displays HrVar, MinVar, Secvar and CycleLength / And it takes which cell to display onto the LCD.
SWC Interface	Time_voidDisplay(u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Certain Position to start write from onto the LCD
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_16_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It adjusts the cursor position at LCD.
SWC Interface	Time_voidAdjustCursor (u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Pointer to Certain Position
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_17_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It increments Hrvar, SecVar and MinVar according to which cell LCD on at this time.
SWC Interface	Time_voidIncr(u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Pointer to Certain Position
Return	Type	Name			Description
	void	_____			_____

### Alarm mode requirements

Req_ID	Req_PO3_DGW_GDD_18_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It displays AlHrVar, AlMinVar, AlSecvar and AlCycleLength / And it takes which cell to display onto the LCD.
SWC Interface	Alarm_voidDisplay(u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Certain Position to start write from onto the LCD
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_19_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It adjusts the cursor position at LCD.
SWC Interface	Alarm_voidAdjustCursor (u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Pointer to Certain Position
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_20_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It increments AlHrvar, AlSecVar and AlMinVar according to which cell LCD on at this time.
SWC Interface	Alarm_voidIncr(u8* Copy_Pu8SetCell)
Parameters	Type	Name			Description
	u8*	Copy_Pu8SetCell			Pointer to Certain Position
Return	Type	Name			Description
	void	_____			_____

### 5.3.3 StopWatch Component

Req_ID	Req_PO3_DGW_GDD_21_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It displays StHrVar, StMinVar, StSecvar. / And it takes which cell to display onto the LCD.
SWC Interface	SW_voidDisplay(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_22_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It checks which press at this time / First press -> start SW -> Set SW_flag = 1 to start increment / Second press -> Stop SW -> Stopwatch_flag = 1 to reset / Thirs press -> Resume SW_flag = 0
SWC Interface	SW_voidCheckStatus(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_23_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It Resets SW_flag and StopWatch_flag
SWC Interface	SW_voidReset(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

### 5.3.4 DGW Requirements

Req_ID	Req_PO3_DGW_GDD_24_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It reads Button 1 switch state and modifies Current_Mode signal to detect which mode is running know (Time or Alarm or Stop Watch) / Current_Mode is a global variable.
SWC Interface	ReadMode(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_25_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It checks Current_Mode signal to choice which to display -> Time or Alarm or Stopwatch. / Current_Mode is a global variable.
SWC Interface	Display(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_26_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It reads Button 2 switch state / If (Pressed) -> Check Current_Mode signal to detect which mode is running know. / If (Current_Mode == 0) -> call Time_voidAdjustCursor() / If (Current_Mode == 1) -> call Time_voidAdjustCursor() / If (Current_Mode == 2) -> call SW_voidCheckstatus() / Current_Mode is a global variable.
SWC Interface	ReadPos(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_27_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It reads Button 3 switch state / If (Pressed) -> Check Current_Mode signal to detect which mode is running know. / If (Current_Mode == 0) -> call Time_voidIncr() / If (Current_Mode == 1) -> call Time_voidIncr() / If (Current_Mode == 2) -> call SW_voidReset() / Current_Mode is a global variable.
SWC Interface	ReadInc(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_27_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It checks Buzzer_signal / If (Buzzer_signal ) -> turn Buzzer on / If (Buzzer_signal) -> turn Buzzer off / Buzzer_signal is a global variable.
SWC Interface	CheckBuzzerState(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Req_ID	Req_PO3_DGW_GDD_28_V01.0		Covers
Responsible for	Norhan Nassar		Date	27/2/2020
Description:	It increments HrVar, MinVar and SecVar every 1 sec by passing this function to the ISR of the timer. / And it checks Current_Mode signal / If(Current_Mode == 1) -> Alarm Mode / So if (HrVar,MinVar and SecVar == AlHrVar, AlMinVar and AlSecVar ) / Buzzer_signal = 1
SWC Interface	TimeInc(void)
Parameters	Type	Name			Description
	void	_____			_____
Return	Type	Name			Description
	void	_____			_____

Table 3 Reference Table
Reference Input Documents	Version	Status
SRS	1.5	Released
HSI	1.5	Released